## Slide 1: Solar Energy
The Tale of an Actual User
Mark Steinmetz

## Slide 2: Solar Energy
About the System
Considerations
  Size
  Location
  Cost Analysis and Payback
  Research
  Production Annual / Monthly Average %
  Things to consider
  Takeaways

## Slide 3: Solar Energy
Commissioning Date; February 15th, 2017
32 Panels - Trina Solar – 335w each– DC
Added 4 additional panels 4/30/2018 for a total of 36
Increased to 12.0 kW
Inverter – Fronius 10kw inverter
Ground Mount

## Slide 4: Solar Energy

## Slide 5: Solar Energy

## Slide 6: Solar Energy

## Slide 7: Solar Energy
Initial Cost Installed $25,000.00
Estimated Annual Production 15,000 kW
Federal Tax Credit @ 30% $7500.00
Solar Renewable Energy Credits
Estimated at 40% of project $10,000.00
Estimated Annual Energy cost savings $ 1,650.00
Estimated simple payback period 4.7 years
Estimated after panel add 4.3 years

## Slide 8: Solar Energy
Research
National Renewable Energy Laboratory - PVWatts Calculator
https://pvwatts.nrel.gov/
Schuler County Hwy Dept.
Schuyler Co. Hwy. Dept. Plant overview (sunnyportal.com)
Commissioned: June 02, 2011
108,736 kWhs produced

## Slide 9: Solar Energy
Production
Total 66,734 kWhs - 4 years
Average annual production
16,390.25 kW

## Slide 10: Solar Energy
Location Considerations

## Slide 11: Solar Energy
Production
Percent of annual production
January 6%
February 5%
March 8%
April 8%
May 10%
June 11%
July 11%
August 10%
September 10%
October 7%
November 7%
December 6

## Slide 12: Solar Energy
Items to think about
Is your home or facility Energy Efficient?
What size system?
Where would I locate the array?
What would be my cost per watt?
Does my utility have a net-metering program?
Are there SREC’s available?
Are there any incentives available from the Utility?
  No residential incentives, IPA handles SREC’s
  Ameren has incentives for Smart Inverters for commercial accounts.

## Slide 13: Solar Energy
Key Takeaways
Always look to energy efficiency projects first!
  Consistent savings and lower usage regardless of source
Compare pricing and use a metric of, “cost per watt”
Source from a trusted provider
Low maintenance
In Illinois – they should not increase property tax value

## Slide 14: Solar Energy
67,040 kWhs to date
Equivalent to CO2 reduction
10.2 Passenger vehicles driven for 1 year
5,334 Gallons of gasoline consumed
52,228 lbs. of coal burned
1801 incandescent lamps switched to LED
47.4 metric tons of Carbon Dioxide

## Slide 15: Solar Energy
Questions